## Slide 1: Grid Watch: Mapping Blackouts with Smart Phones
Noah Klugman*, Javier Rosa**, Pat Pannuto*, Matthew Podolsky**, William Huang*, Prabal Dutta*
University of Michigan*
University of California, Berkeley**
HotMobile 2014 – Febuary 26th, 2014
Notes: Add uc logo

## Slide 2: Making “dumb” smart.
photo: www.extremetech.com
Notes: Andrew
Automate an important process
Expose new information
Inform the public

## Slide 3: The health of the power grid is not well understood.
Generation
Transmission
Distribution
Monitor
Source
Notes: Most complex thing we have ever built
No transparency
Power companies have this data at the substation level, but this isn’t much use to researchers
smart meter (get stats, internationally->steal it vs smart card)
Grid watch idea here, vague
(generation, transmission, distribution)
Set up infrastructure with monitor

## Slide 4: How It Works In Ann Arbor
Energy
Company
Is your power out?
Energy
Company
Ok. Thank you.
Yes. And I’m cold.
T+0 Power Goes Out
.
.
.
T+12h Energy Company Call
Energy
Company

## Slide 5: How It Works In Ann Arbor
T+0 Power Goes Out
.
.
.
T+12h Energy Company Call
Is your power out?
Ok. Thank you.
Yes. And I’m cold.
.
.
.
T+36h Call Energy Company
We’re aware and working on it.
My power is still out.
.
.
T+60h Energy Company Call
Is your power still out?
Ok. It will be back soon.
Yes. And I’m very cold.
.
.
T+72h Call Energy Company
Are you sure?
We’ll send someone to investigate ASAP
My power is still out.
It’s been 3 days.
.
.
T+80h Energy Company Call
Is your power back on?
No. Still no power.
3 days and several phone calls later…
T+152h Call Energy Company
That’s great. We’re sorry for the inconvenience.
Calling to let you know my power is finally back.
.
.
T+160h Energy Company Call
Hi! Just calling to see if your power is back on yet?
Great! Thanks for letting us know!
Yes. It is.
Notes: “While some of this can be attributed to the chaos of a large outage, there is very clearly still a problem”

## Slide 6: How It Works In Ann Arbor
T+0 Power Goes Out
.
.
.
T+12h Energy Company Call
Is your power out?
Ok. Thank you.
Yes. And I’m cold.
.
.
.
T+36h Call Energy Company
We’re aware and working on it.
My power is still out.
.
.
T+60h Energy Company Call
Is your power still out?
Ok. It will be back soon.
Yes. And I’m very cold.
.
.
T+72h Call Energy Company
Are you sure?
We’ll send someone to investigate ASAP
My power is still out.
It’s been 3 days.
.
.
T+80h Energy Company Call
Is your power back on?
No. Still no power.
3 days and several phone calls later…
T+152h Call Energy Company
That’s great. We’re sorry for the inconvenience.
Calling to let you know my power is finally back.
.
.
T+160h Energy Company Call
Hi! Just calling to see if your power is back on yet?
Great! Thanks for letting us know!
Yes. It is.
And this home has a smart meter installed…
Notes: “While some of this can be attributed to the chaos of a large outage, there is very clearly still a problem”

## Slide 7
photo: Rajesh Kumar Singh/Associated Press
Notes: Power grid failure in india… 600 million people
Show two extremes, distribution of power outages, extent and frequency and duration

## Slide 8: Detecting Power Outages With Smartphones
Notes: Top level
When phones are unplugged
Everyone already installs for us
Show phone in the middle of the power grid and the cell network

## Slide 9: We propose a global, crowd-sourced platform that leverages a simple side-channel available to smartphones—the charger status—to provide a simple, free, and easily deployable grid monitoring solution.
Notes: Using this crowd sourcing technique, unmodified phones with present sensors we can …
Use a claim
Then why is this
The phone can observe 1 and report over 2

## Slide 10: Crowd-Sourced Monitoring is Useful to Ratepayers, Researchers and Regulators
People want to know
How often does power go out in a neighborhood?
Is Eggman Electric more dependable than OmniCorp Power?
Where is the data to inform regulators that power is unreliable?
Notes: Another channel
Calling power companies to ask for this and say no
No public available repo of outage data, especially not indepent of utility
Enable third parties – ratepayers, researchers and regulators, hold utilities responsible

## Slide 11: Grid Watch

## Slide 12: Architecture: Grid Watch System
Server
Grid Watch is woken up when charge state changes
Heuristics are used to filter out false positive events
When a true event is detected, data is gathered and sent to a central service
Data is displayed to the user and made available for download
Report
Filters
Displays
Notes: Dig into each piece

## Slide 13: Architecture: Charge State
OS subscribe to notification
Can wake up App on change
Timestamp at this point
Server
!
Report
Filters
!
Displays

## Slide 14: Architecture: False Positive Filters
Server
!
Report
Filters
Displays
Accelerometer
Microphone
Additional Heuristics
Threshold
Threshold

## Slide 15: Architecture: False Positive Filters: Accelerometer
Server
!
Report
Filters
Displays
People pick up the phone to unplug it
Low energy

## Slide 16: Architecture: False Positive Filters: Microphone
Server
!
Report
Filters
Displays
The microphone can detect AC mains
Higher energy

## Slide 17: Architecture: Filters: AC Mains Detection FFT
5 second recording
44.1 k, 16 bit
Sliding aggregate
1 sample window

## Slide 18: Architecture: Filters: Noisy AC Mains Detection
Notes: Relative amp is low

## Slide 19: Architecture: Filters: Additional Heuristics
Presence of WiFi
Audio context detection
External data (eg weather reports, power company sites)
Notes: Relative amp is low

## Slide 20: Architecture: Uplink
Server
!
Report
Filters
Displays
GPS location, Unique ID, Timestamp
Local cache of outages
HTTP POST and SD log
Notes: Only sample GPS after filters
Cache outage

## Slide 21: Architecture: Central Service
Server
!
Report
Filters
Displays
Gathered into DB for further analysis
Indexed by phone, supports deletion and correction

## Slide 22: Research Questions

## Slide 23
Can all mobile platforms support Grid Watch?
How do we cope with sensor diversity?
What noise does this create in the aggregate?
Research Questions: Does Smartphone Diversity Impact Grid Watch?

## Slide 24
How many phones must report in an area?
How will population dynamics change readings?
How can we incentivize use?
Research Questions: How Much Grid Must Grid Watch Watch if Grid Watch Could Watch Grid?
Notes: Second session of the day, Phone Lab at the University of Buffallo

## Slide 25: Research Questions: Can We Identify Outliers?
How can we sanitize Grid Watch data?
  Faulty phones, bad actors, unfortunate homes
Notes: Spatial temporal Clustering

## Slide 26: Research Questions: Can Grid Watch Expose Complex Grid Events?
Can we track more complex grid behaviors?
How to process huge data, real time?
Higher resolution FFTs?
External sensors?
Notes: Provide the strawman
Speculate on pre failure
Change to real questions
Huge data, real time

## Slide 27: Research Questions: Can Grid Watch Expose Complex Grid Events?
Notes: Ten phones, six models, 20 trials
Avg std dev is .76 s between reports of an identical outages
19 out of 20 trials, standard deviation less than .8 seconds
Cascading outages spread in minutes
3g, a mix of networks
Histogram not the way to show this

## Slide 28: Research Questions: Privacy
How can we best preserve privacy?
What granularity location data is needed for meaningful analysis?
Photo: NPR

## Slide 29: Deployment

## Slide 30: Initial Deployments
15 phones
Mid-March
Kenya
Ann Arbor
Lab phones, eventually Play Store
http://inductor.eecs.umich.edu/gridwatch.html

## Slide 31: Grid Watch
Propose a simple, scalable, grid monitoring solution deployable independently of utility companies
Require no additional infrastructure
Demonstrate the feasibility of false positive filters
Identify key research questions for future work
Noah Klugman
University of Michigan
nklugman@umich.edu